## Slide 2
Engino.com
Engino Robotics Platform
  Στόχοι
  Εύκολος τρόπος μάθησης προγραμματισμού.
  Κατανόηση των βασικών εννοιών προγραμματισμού και ρομποτικής.
  Μάθηση του τρόπου σκέψης για επίλυση προβλημάτων.(Task ,Think ,Action).
  Παιχνίδι ->Δημιουργία ->Μάθηση .“Play to Invent”
Τι είναι προγραμματισμός;
«Είναι το σύνολο των διαδικασιών σύνταξης ενός υπολογιστικού προγράμματος για την πραγματοποίηση εργασιών ή για την επίλυση ενός δεδομένου προβλήματος». -Wikipedia-

## Slide 3
32-bit ARM CORTEX-M2 micro controller
256 Kbytes FLASH, 64 Kbytes RAM
USB full speed port (12 Mbit/s)
7 input-output ports.
Onboard buzzer.
3 Motor output ports manually programmable for forward and reverse.
2 LED outputs manually programmable for ON-OFF.
Power source: 6 AA batteries.
Pro version includes WIFI.
Engino Robotics Platform Speciﬁcations:

## Slide 4
Engino Controller
FIRST OUT
Δίοδοι Εκπομπής Φωτός LED
Μοτέρ
Αισθητήρας IR
Διακόπτης

## Slide 5
Engino.com
ERP simulator
ERP Software
Function Blocks
Text Editor

## Slide 6
ERP SIMULATOR

## Slide 7
Flow View Diagram
Start
FIRST OUT
LED Properties
PORT A,B,C,1,2,3,4 Time 1-Forever
State ON,OFF
Delay 0- Infinity
WITH/AFTER Previous
01101011010
Repeat 1-Forever
Motor Properties
PORT A,B,C Time 1-Forever
State LEFT,RIGHT,OFF
Delay 0- Infinity
WITH/AFTER Previous
Speed 1-100
Idle Properties
Time 1-Forever
Buzzer Properties
Time 1-Forever
State ON,OFF
Delay 0- Infinity
WITH/AFTER Previous

## Slide 8
Pseudocode vs Engino Blocks
Public void Start(Forever)
{
if(Sensor.Port1==State.ON)
{ LED(Port2,State.ON,5) }
}
LED Properties
PORT 2 Time 5
State ON
Delay 0
AFTER Previous
Sensor Properties
PORT 1 State ON

## Slide 9
Pseudocode vs Engino Blocks
Public void Start(Forever)
{
if(Sensor.Port1==State.ON)
{ LED(Port2,State.ON,5) }
}

## Slide 10
Pseudocode vs Engino Blocks
Public void Start(Forever)
{
while(Sensor.Port1 is State.ON)
{ LED(Port2,State.ON,5) }
}
LED Properties
PORT 2 Time 5
State ON
Delay 0
AFTER Previous
Sensor Properties
PORT 1 State ON
useless

## Slide 11
Pseudocode vs Engino Blocks
Public void Start(Forever)
{
while(Sensor.Port1 is State.ON)
{ LED(Port2,State.ON,5) }
}

## Slide 12
Logical Gates
Public void Start(Forever)
{
while(Sensor.Port1 is State.ON AND Sensor.Port3 is State.ON )
{ LED(Port2,State.ON,5) }
}

## Slide 13
Logical Gates
Public void Start(Forever)
{
while(Sensor.Port1 is State.ON OR Sensor.Port3 is State.ON )
{ LED(Port2,State.ON,5) }
}

## Slide 14
EnginoRobotics.com